Retro-Fit all non com-pliant equipment

Table saws need to have proper guards

Barrier devices create a safety buffer for employees

Environmental Health, Safety & Emergency Management

Toolbox Talk

MACHINE GUARDING

This Toolbox Talk is based on OSHA’s machine guarding standards. Guarding in-valves protecting ourselves from machines and equipment in our work environment.

Basic Terminology:

Parts of the Machine Requiring Guarding

Point of Operation: Area where machine performs work on material

Power Transmission Apparatus: Belts, gears, flywheels, chains, pul-leys, spindles, couplings, cams, machine components that transmit energy.

Other Moving Parts: Reciprocating, rotating, traversing motions, auxil-iary machine parts.

Types of Mechanical Motion that Must be Guarded:

Pinch Points: Points at which it is possible to be caught be-tween moving parts, or between moving and stationary parts of a piece of equipment

Rotating: Circular motion of shafts with a protrusion sticking out can grip clothing or pull body part into point of operation

Reciprocating: Back-and -forth or Up-and-Down motion that may trap/ strike an employee between the moving object and a fixed object. Traversing: Movement in straight, continuous line that may strike or catch an employee in a pinch or shear point between a moving and fixed object.

Cutting: Action of sawing, boring, drilling, milling, slicing

Punching: Action resulting when a machine moves a slide (ram) to stamp a sheet of metal or other material.

Shearing: Movement of a powered slide or knife during metal trimming or paper cutting

Bending: action occurring when power is applied to a slide to draw or form metal or other materials

Common Machines That Require Machine Guards:

| Circular Saw | Reciprocating Saw | Band Saw | Jointer |
| --- | --- | --- | --- |
| Power Feed Planer | Shaper | Lathe | Sander |
| Drill Press | Grinding Wheels | Mechanical Power | Mortising Machine |
|  |  | Press |  |

Group Discussion Topics:

Identify the machines in your shop or that you use that require machine guarding.

How could someone be injured by using these machines? How can this be prevented?

Inspect your machines to ensure the guards are correctly positioned, intact and in place.