Fall protection—Basic types

List fall hazards on site. ___________________________________ ___________________________________ ___________________________________ ___________________________________ ___________________________________

Explain dangers

Falls are the number-one cause of accidental deaths in construction. And you don’t have to fall far to be killed or injured.

Identify controls

On many sites, guardrails are the most common and convenient means of fall protection. Where guardrails cannot be installed or are impractical, the two basic types of fall protection are travel restraint and fall arrest. Both involve a full-body harness.

Travel restraint system

A travel restraint system keeps you from getting too close to an unprotected edge.

The lifeline and lanyard are adjusted to let you travel only so far. When you get to the open edge of a floor or roof, the system holds you back and prevents you from falling.

A full-body harness should be used with travel restraint systems. You can attach the harness with a lanyard that attaches to a rope grab on the lifeline. The lifeline must be securely anchored.

Fall arrest system

If no other fall protection is in place, you

must use a fall arrest system if you are in danger of falling:

- more than 3 metres

- into operating machinery

- into water or another liquid

- into or onto a hazardous substance or object.

A fall arrest system consists of a full-body harness, a lanyard, and a shock absorber.

You can connect the lanyard directly to adequate support OR to a rope grab mounted on an adequately anchored lifeline.

A full-body harness must also be worn and tied off when you are:

- on a rolling scaffold that is being moved

- getting on, working from, or getting off a suspended platform, suspended scaffold, or bosun’s chair.

Lifelines must be adequately anchored. For fall arrest, that means able to support the weight of a small car (about 3,600 pounds).

Demonstrate

Show how to put on, adjust, and wear a full-body harness.

Full-Body Harness

20	                                      Working at Heights