Stepladders

List stepladder locations on site. ___________________________________ ___________________________________ ___________________________________ ___________________________________ ___________________________________ ___________________________________ ___________________________________

Explain dangers

The stepladder is one of the most familiar things on a jobsite. Still, workers get hurt using them.

Falls are the biggest risk. Even though workers are not very high off the ground, some have died from falling a short distance and landing the wrong way. Even sprains or strains could mean pain and days off work.

Identify controls

[Use a stepladder to demonstrate as you talk.]

Here’s how to use a stepladder the right way.

• Check the ladder for defects or damage

–– at the start of your shift

–– after it has been used somewhere else by other workers

–– after it has been left in one place for a long time.

- Keep the area at the base of the ladder clear.

- Make sure the spreader arms lock securely in the open position.

- Stand no higher than the second step from the top.

- Never straddle the space between a stepladder and another point.

Stepladder

- When standing on the ladder, avoid leaning forward, backward, or to either side.

- Always open the ladder fully before using it. Don’t use an unopened stepladder as a straight or extension ladder. The feet are not designed for this use.

- Never stand on the top step, the top, or the pail shelf of a stepladder.

- When climbing up or down a stepladder, always face the ladder and maintain 3-point contact. That means two hands and one foot or two feet and one hand must be on the ladder at all times.

Demonstrate

Inspect stepladders in use on site. Determine whether other equipment would provide safer, more efficient access.

| Working at Heights | 23 |
| --- | --- |