| Picture of task/equipment: | Task: | Chemical use |
| --- | --- | --- |
|  | Name of Shop or Dept: | Dining Services, Rooms |
|  | Job Title(s): | All |
|  | Analyzed by: | M. Williams |
|  | Date: | 01/30/13 |
| Required PPE: |
| Face Shield Neoprene, Butyl, Rubber gloves Chemical resistant Apron |
| Required/Recommended Trainings: |
| Hazard Communication |
| TASK | HAZARDS | CONTROLS |
| Mixing chemicals for operational use | Chemical Burns Face Eyes Skin Ingestion Inhalation | Always review MSDS prior to mixing chemicals. Always check for incompatibles, such as acids and bases. Never mix incompatible chemicals; Mixing incompatibles can increase hazards, such as creating a vapor and inhalation hazard from mixing acids with bases Don PPE to minimize risk of exposure to skin Only use chemicals that you have been trained on using and are familiar with. When using an acid product (bathroom cleaners, lime based cleaners) always add acid to water, never the other way around. Only use chemicals that are properly labeled and do not use more than necessary. Immediately replace cap/lid as soon as you are done with the chemical. Use a compatible container (HDPE/mop bucket) with the chemical when mixing. |

|  | Injury & Illness Prevention Program Job Safety Analysis Form |
| --- | --- |