Extension ladders

Explain dangers

Extension ladders can be dangerous tools. Workers have been killed and injured from falls and powerline contact.

Identify controls

- Choose the right ladder for the job. It must be long enough to

–– be set up at a safe angle (see below)

–– extend 90 centimetres (3 feet) beyond the top landing.

  - A two-section extension ladder should be no longer than 15 metres (50 feet); a three-section ladder no longer than 20 metres (66 feet).

- Check the ladder for damage or defects

––before you set it up

––after it has been used somewhere else by other workers

––after it has been left somewhere for a long time.

- Set the ladder on a firm, level base. If the base is made of soft, loose, or wet material, clear it away or stand the ladder on a mud sill.

- Never erect extension ladders on boxes, carts, tables, or other unstable objects. Never stand them up against flexible or movable surfaces.

- Set the ladder up at a safe angle—one foot out for every three or four feet up, depending on length.

- When the ladder is set up, there should be a clear space of at least 15 centimetres or

6 inches behind each rung.

- When the ladder is fully extended, sections must overlap at least 90 centimetres (3 feet).

- Stand no higher than the fourth rung from the top.

- Tie off or otherwise secure the top and bottom of the ladder. Keep areas at the top and bottom clear of debris, scrap, material, and other obstructions.

- Clean mud, snow, and other slippery substances off your boots before climbing.

- When climbing up or down, always face the ladder and maintain 3-point contact.

- Don’t carry tools, equipment, or material in your hands while climbing. Use a hoist line or gin wheel for lifting and lowering.

- Be very careful when erecting extension ladders near live overhead powerlines. Never use metal or metal-reinforced ladders near electrical wires or equipment.

- Wherever possible, use extension ladders only for access—not as work platforms.

- When you must work from a ladder more than 3 metres or 10 feet up, wear a safety harness and tie off to a well-anchored lifeline or other support—not to the ladder.

Demonstrate

Demonstrate as you talk.

24	                                      Working at Heights