Scaffolds—Planks and decks

List scaffolds needing inspection on site. ___________________________________ ___________________________________ ___________________________________ ___________________________________ ___________________________________ ___________________________________

Explain dangers

If scaffold planks and decks fail, you could be seriously injured or killed from a fall. You could also be thrown off balance and injure yourself with your tools or equipment.

Identify controls

Scaffold planks and deck material must be inspected regularly. Here’s what to check for.

Wood planks

- Length—planks must overhang the frame no less than 6 and no more than 12 inches (150 – 300 mm).

- Cracks—often be detected at the end of the plank. Discard planks with long and deep cracks.

- Cuts—check plank edges for cuts from saws, tools, and sharp objects. Discard planks with many or deep cuts.

- Plank defects—worm holes, splits, knots that are knocked out along edges, and lots of nail holes. Discard planks when defects are serious.

- Light weight—this can indicate dry rot that can’t be seen.

- Damaged cleats—they should be removed and replaced.

Plank defects

Laminated veneer lumber planks

- Separation of laminated layers—this is usually due to repeated changes in moisture levels as layers soak up rain and dry in sun.

- Cuts of any kind.

- Pressure cracks in the top or bottom layer.

- Warping from wear and weather.

- Damaged cleats.

Aluminum/plywood deck panels

- Cuts in aluminum frames.

- Deformed, cracked, or broken fastening hooks and hardware.

- Cracked or broken plywood.

- Bent, cracked, or broken rungs.

- Sliding or other locking devices in good condition.

As a general rule, you should plank or deck the working levels of a scaffold across their full width for maximum support and stability.

Demonstrate

Demonstrate methods of inspecting planks and panels. Ask crew to inspect sample materials on site.

| Working at Heights | 27 |
| --- | --- |