Scaffolds—Structural components

List scaffold locations on site. ___________________________________ ___________________________________ ___________________________________ ___________________________________ ___________________________________ ___________________________________

Explain dangers

If scaffold components are damaged, defective, or installed incorrectly, it can lead to tip-over or collapse.

Demonstrate

Demonstrate as you talk.

Structural components of all frame scaffolds must be inspected regularly. Inspection should include frames, feet, connecting pins, braces, and guardrails.

Frames

- Uprights and cross-members should not be cracked, rusty, bent, or otherwise deformed.

- All connecting components should fit together square and true.

Feet

- Adjustable base plates should work properly.

- Plates should be securely attached to legs to resist uplift as well as compression.

- If mudsills are used, base plates must be nailed to them.

Connecting pins

- Frames must be joined together vertically by connecting pins compatible with the frames.

- Connecting pins must be locked in place to prevent them from loosening and coming out.

- Pins must be free of bends and distortion. If they don’t fit, get replacements that do.

Braces

- Cross and horizontal braces should not be cracked, rusty, bent, or otherwise deformed.

- Braces should be compatible with frames and free of distortion.

- Horizontal braces must be installed every third frame vertically and in each bay laterally.

- Scaffolds higher than three frames must be tied into the structure.

Guardrails

- The work platform must have guardrails.

- Guardrails must be compatible with frames.

- Guardrails can be made of tube-and-clamp components if they’re assembled properly.

28	                                      Working at Heights